AN EPROM PROGRAMMER FOR THE BIG BOARD
			 written by Jim Monesmith
			 438 Patterson Road
			 DAYTON, OHIO 45419

	If you ever have a need to program a 2708, 2716, or 2732 eprom then
this article is for you. The article is presented in four parts. they are
construction, bigboard jumpers, software, and operation documentation. I am
noting at this time that the object code listing presented in the software
section is for a 4 MHz. CPU clock bigboard. If you are using a 2.5 MHz. CPU
bigboard you will have to change the sofware timing loops for the one mille
second and the 50 millesecond programming pulses. See the source listing for
these changes. Another option is to modify your slow bigboard. If you chose
this second option then be sure to use the 4 MHz. PIO, SIO, CTC, and CPU
devices. The second issue of this publication will show you more details
on this modifaction.


		PART I     PROGRAMMER AND POWER SUPPLY CONSTRUCTION

	Using the eprom programmer parts list, and the accompaning schematic
construct the programmer on a wire wrap board of your choice. Don't forget to
use decoupling capacitors between Vcc and ground (.01 micro farad cap. per ic) 
even though they are not shown on the schematic. Also use three 15 micro farad 
tantalum electrolytic capacitors between the plus five volt supply and ground. 
Observe polarity with the + lead connected to Vcc and the other lead connected
to ground. Using connectors of your choice construct a cable to attach the
programmer to the bigboard connector J5 with the following pin designations:

	PROGRAMMER SIGNAL NAME		  BIGBOARD PIN NUMBER

	    DATA BIT 0-----------------------J5 PIN 6
	    DATA BIT 1-----------------------J5 PIN 8
	    DATA BIT 2-----------------------J5 PIN 10
	    DATA BIT 3-----------------------J5 PIN 12
PORT A	    DATA BIT 4-----------------------J5 PIN 14
	    DATA BIT 5-----------------------J5 PIN 16
	    DATA BIT 6-----------------------J5 PIN 18
	    DATA BIT 7-----------------------J5 PIN 20

	    CLOCK----------------------------J5 PIN 26
	    PGM------------------------------J5 PIN 30
PORT B	    PROG-----------------------------J5 PIN 32
	    VERIFY---------------------------J5 PIN 34
	    RESET----------------------------J5 PIN 36

	    GROUND---------------------------J5 PIN 1
	    GROUND---------------------------J5 PIN 3

	Using the power supply schematic and the power supply parts list,
construct the power supply on a prototype card of your choice. Be sure to
observe polarity of the electrolytic capacitors. Correct polarity for the
positive supplies is for the + lead to go to the positive side of the supply,
and the other lead to ground. For the -5 volt supply the + lead should go to
ground, and the other lead to the -5 volt supply. Be sure and mount LM340T-5
plus five volt regulator and the LM317T adjustable positive voltage regulator
on heat sinks, using heat sink grease. The LM340T-12 twelve volt regulator
and the LM320T-5 minus five volt regulator do not require heat sinks.
	Now you need to fabricate the personality modules. On separate 16 pin
dip headers make the following jumper connections for the personality modules:

				pin 1 to pin 16
2716 PERSONALITY MODULE		pin 2 to pin 15
				pin 3 to pin 14


ON A SEPARATE 16 PIN HEADER:


				pin 4 to pin 13
2732 PERSONALITY MODULE		pin 6 to pin 11
				pin 7 to pin 10

	Next mount the 24 pin textool zero insertion force sockets to two
24 pin dip headers. This will make their attachment to the rest of the circuit
simpler.
 	The final step in the construction of the programmer is to adjust the
programming voltage. This is accomplished by adjusting R19 (the pot in the
power supply section) while the program is running menu selection number 6
WITH NO EPROMS IN THE PROGRAMMING SOCKETS !!!!!!!!!  R19 is adjusted until
the voltage at test point TP-1 is exactly 25.5 volts. Be sure to use a very
accurate high impedance meter for this adjustment.
	This completes the construction section as the 2708 eprom does not
require a personality module.
	I might add at this point that with the voltage set at 25.5 volts
the programmer will program Intel 2708's, Intel 2716's, and Intel 2732's, or
any device that meets their respective specifications.


			NOTE THIS WELL !!!!!!!!!!!!!!!!!!!!!

	IF YOU WANT TO PROGRAM AN INTEL 2732A EPROM YOU WILL HAVE TO LOWER
	THE PROGRAMMING VOLTAGE AT TP-1 TO 21 VOLTS. INTEL CHANGED THE
	SPEC. ON THE 2732A PROGRAMMING VOLTAGE FROM 25 VOLTS TO 21 VOLTS.
	THE 2732A WILL BE DAMAGED IF YOU TRY TO PROGRAM IT AT 25.5 VOLTS !

		   	    YOU HAVE BEEN WARNED.




       	EPROM PROGRAMMER PART LIST

NUMBER		DESCRIPTION

  1		  PROTOTYPE BOARD OF YOUR CHOICE
  1		  74LS00  2 INPUT NAND GATE
  1		  7407    OPEN COLLECTOR BUFFER WITH HIGH VOLTAGE OUTPUTS (30V)
  1		  74LS04  HEX INVERTER
  1		  MC14040B 12 BIT BINARY COUNTER (MOTOROLA)
  1		  8286     BI-DIRECTONAL BUFFER (INTEL)
  2		  2N2222A  NPN TRANSISTOR
  2		  2N3906   PNP TRANSISTOR
  3		  2N3904   NPN TRANSISTOR
  1		  1N914    DIODE
  2  	   	  24 PIN ZERO INSERTION FORCE SOCKET (TEXTOOL 224-3344)
  2		  24 PIN WIRE WRAP SOCKET
  2		  24 PIN DIP HEADER
  1		  20 PIN WIRE WRAP SOCKET
  5		  16 PIN WIRE WRAP SOCKET
  2		  14 PIN WIRE WRAP SOCKET
  4		  16 PIN DIP HEADER
  2		  3K   OHM RESISTOR 1/4 WATT  5%
  1  		  27K  OHM RESISTOR 1/4 WATT  5%
  1		  620  OHM RESISTOR 1/4 WATT  5%
  1		  1K   OHM RESISTOR 1/4 WATT  5%
  1		  2.7K OHM RESISTOR 1/4 WATT  5%
  3		  10K  OHM RESISTOR 1/4 WATT  5%
  2		  50   OHM RESISTOR 1/4 WATT  5%
  1		  5.1K OHM RESISTOR 1/4 WATT  5%
  1		  11K  OHM RESISTOR 1/4 WATT  5%
  1		  3.6K OHM RESISTOR 1/4 WATT  5%
  2		  2.2K OHM RESISTOR 1/4 WATT  5%
  2		  0.1  MICRO FARAD CAPACITOR  50 VOLT CERAMIC
  10		  0.01 MICRO FARAD CAPACITOR  50 VOLT CERAMIC
  2		  1.0  MICRO FARAD CAPACITOR  50 VOLT  TANTALUM ELECTROLYTIC
  1		  .004 MICRO FARAD CAPACITOR  50 VOLT CERAMIC
  

        POWER SUPPLY PART LIST

NUMBER		DESCRIPTION

  1		  PROTOTYPE BOARD OF YOUR CHOICE
  1		  25.2 VOLT TRANSFORMER RADIO SHACK NUMBER RS-273-1505
  1		  12.6 VOLT TRANSFORMER RADIO SHACK NUMBER RS-273-1480
  8		  1N4005 DIODE
  3		  100 MICRO FARAD CAPACITOR ELECTROLYTIC 50 volt
  1		  1000 MICRO FARAD CAPACITOR ELECTROLYTIC 50 volt
  4		  1.0 MICRO FARAD CAPACITOR TANTALUM ELECTROLYTIC 50 volt
  1		  5K OHM POT
  1		  200 OHM RESISTOR 1/4 WATT  5%
  1		  LM317T ADJUSTABLE VOLTAGE REGULATOR
  1		  LM340T-5   +5 VOLT REGULATOR
  1		  LM340T-12  +12 VOLT REGULATOR
  1		  LM320T-5   -5 VOLT REGULATOR



		PART II		BIGBOARD JUMPERS
	
	I also assume that your bigboard has the PIO parallel option installed 
in it. You will also need two 74LS243 I.C.s installed in sockets U90 and U92 of
the PIO section. ON two separte 14 pin headers jumper the following pins, and 
install the headers in sockets U91, and U93:

			pin 6 to pin 8
			pin 5 to pin 9
			pin 4 to pin 10
			pin 3 to pin 11

also jumper JB3 pin 16 to JB3 pin 14 now, jumper JB3 pin 14 to J5 pin 40. This
last connection uses bit 7 on PIO port B to control the direction of the bi-
directional buffers in U90 and U92. The eprom data is output and input on port
A of the general purpose PIO. The general purpose PIO port B is used to control
the programmer, with the following control signal designations:

		BIT 0		CLOCK (ACTIVE HIGH)
		BIT 1		NOT USED
		BIT 2		PROGRAMMING PULSE (ACTIVE LOW)
		BIT 3		PROGRAMMING MODE (ACTIVE LOW)
		BIT 4		VERIFY MODE (ACTIVE LOW)
		BIT 5		RESET (ACTIVE LOW)
		BIT 6		NOT USED
		BIT 7		BUFFER DIRECTION CONTROL (0=OUTPUT 1=INPUT)


		PART III	SOFTWARE

		Refer to the program listing. The program is very heavily
	commented and should be self-explanatory. The program has been in use
	for quite some time now, and I believe it to be completely bug free. 
		At this time I will present an object code dump of the program 
	for quick entry of the program into your machine. The code entry should
	start at 0100 hex. After you have completed the entry, using DDT.COM,
	type ^C and use the SAVE command to place the program onto your disk. 

		EXAMPLE:
			DDT.COM
			S100
			ENTER THE DATA FROM THE OBJECT CODE LISTING
			^C
			SAVE 11 PROMPIO.COM

	If your typing is accurate you will now have a working copy of the
	eprom programmer sofware on disk.
	If you are lazy, like myself, and do not want to type all of that
	code in by hand, send me $5.00 for handling and an IBM compatable 8"
	single density disk, and I will send you an assembled copy of the
	program along with source code for the program. Don't forget to 
	include your return address and postage for the return trip. I can't
	return your disk unless you include the postage for the return trip.
	The package used to send the disk to me must be usable for the return
	trip also.

	


		PART IV 	OPERATION DOCUMENTATION

2708 READ:
	Place the 2708 eprom in socket number one, then
	type 1. The program will then read the contents of the eprom into
	memory starting at location 4000 hex. 

2708 COMPARE:
	Place the 2708 eprom in socket number one and type 2. The program
	will read the contents of the eprom into memory, starting at location
	3000 hex. After the eprom is read into memory a comparison is made with
	data starting at memory location 4000 hex. If any differences are found
	the program outputs the location in the eprom, that dosen't compare 
	with memory, the data that was read from the eprom, and what the eprom 
	data should have actually been. 

2708 PROGRAM:
	Place the 2708 eprom in socket number one and type 3. The routine will
	will program the 2708 with memory data starting at memory location 4000
	hex. When the programming is complete (about two minutes) the routine
	will enter the verify mode and read the eprom data into location 3000
	hex. A byte by byte comparision will then be made and any differences
	will be reported to the console. If the data in the eprom compares with
	memory, this will also be reported to the console.

2716 READ:
	First place the 2716 personality module in the personality socket. Then
	place the 2716 eprom in socket number two and type 4. The program will
	then tell you to make sure that the 2716 personality module is in the
	personality socket and wait for a space to be typed at the console.
	When the program receives a space, it will proceed to read the 2716
	data into memory starting at location 4000 hex.

2716 COMPARE:
	First place the 2716 personality module in the personality socket. Then
	place the 2716 eprom in socket number two and type 5. The program will
	then tell you to make sure that the 2716 personality module is in the
	personality socket and wait for a space to be typed at the console.
	When the program receives a space, it will proceed to read the 2716
	data into memory starting at location 3000 hex. After the eprom data
	is read into memory, a byte by byte comparision will be made with data
	starting at memory location 4000 hex. If any differences are found the
	program will report them to the console. If the eprom data compares 
	with the memory data, this will also be reported to the console.

2716 PROGRAM:
	First place the 2716 personality module in the personality socket. Then
	place the 2716 eprom in socket number two and type 6. The program will
	then tell you to make sure that the 2716 personality module is in the
	personality socket and wait for a space to be typed at the console.
	When the program receives a space, it will tell you to turn on the
	programming voltage, and wait for another space. When the program
	receives the second space, it will proceed to program the eprom with
	memory data starting at location 4000 hex. After the 2716 is completly
	programmed, the routine will tell you to turn off the programming
	voltage, and wait for a space to be typed at the console. After a space
	is received, the routine will enter the verify mode and read the eprom
	data into memory starting at location 3000 hex. Finally, a byte by byte
	comparision is made with memory starting at location  4000 hex, and any
	differences reported to the console. If the data read from the eprom
	compares with memory data at location 4000 hex, this will also be
	reported to the console.

2732 READ:
	First place the 2732 personality module in the personality socket. Then
	place the 2732 eprom in socket number two and type 7. The program will
	then tell you to make sure that the 2732 personality module is in the
	personality socket and wait for a space to be typed at the console.
	When the program receives a space, it will proceed to read the 2732
	data into memory starting at location 4000 hex.

2732 COMPARE:
	First place the 2732 personality module in the personality socket. Then
	place the 2732 eprom in socket number two and type 8. The program will
	then tell you to make sure that the 2732 personality module is in the
	personality socket and wait for a space to be typed at the console.
	When the program receives a space, it will proceed to read the 2732
	data into memory starting at location 3000 hex. After the eprom data
	is read into memory, a byte by byte comparision will be made with data
	starting at memory location 4000 hex. If any differences are found the
	program will report them to the console. If the eprom data compares 
	with the memory data, this will also be reported to the console.

2732 PROGRAM:
	First place the 2732 personality module in the personality socket. Then
	place the 2732 eprom in socket number two and type 9. The program will
	then tell you to make sure that the 2732 personality module is in the
	personality socket and wait for a space to be typed at the console.
	When the program receives a space, it will tell you to turn on the
	programming voltage, and wait for another space. When the program
	receives the second space, it will proceed to program the eprom with
	memory data starting at location 4000 hex. After the 2732 is completly
	programmed, the routine will tell you to turn off the programming
	voltage, and wait for a space to be typed at the console. After a space
	is received, the routine will enter the verify mode and read the eprom
	data into memory starting at location 3000 hex. Finally, a byte by byte
	comparision is made with memory starting at location  4000 hex, and any
	differences reported to the console. If the data read from the eprom
	compares with memory data at location 4000 hex, this will also be
	reported to the console.

READ A .COM FILE INTO MEMORY AT LOCATION 4000 HEX:
	Type a : at the console. The program will then ask you for the file
	name. Enter the file name, with optional drive indicator. If no drive
	is specified the routine will attempt to read the file from the
	currently logged drive. If a drive is specified the routine will read
	the file from the specified drive. If the file is not found, an error
	message will be typed at the console. The file must be of type .COM.
	The file also must be small enough to fit in the file buffer. The file
	buffer starts at memory location 4000 hex and continues up to location
	D3FF hex. The top address is just before the console command processor
	(CCP). If the file is to large to fit in the file buffer, it must be
	split into two, or more files and read into the buffer one at a time.
	Use the DDT.COM program supplied by DIGITAL RESEARCH INC. with the
	CP/M (tm) disk and the SAVE command to split the file.

    	    EXAMPLE:

		DDT FILENAME.COM
		^C
		SAVE 144 FILE1.COM
		DDT FILENAME.COM
		M9000,D3FF,0100
		^C
		SAVE 68 FILE2.COM


MOVE NEXT BLOCK OF DATA INTO POSITION TO BE PROGRAMMED:
	Type a 0 at the console. The program will then ask what size block
	of data if to be moved. The size of the block will depend on the eprom
	being used. Type 1 for a 2708 eprom, 2 for a 2716 eprom, and 3 for a
	2732 eprom. After receiving a 1,2, or 3 the routine will add the block
	size to 4000 hex to calculate the starting address of the block move.
	The routine will then do a block move using the calculated address
	as the source address for the move, and 4000 hex as the destination
	address for the move. Control will then be passed back to the main
	menu.

SAVING THE CONTENTS OF AN EPROM:
	Read the eprom into memory using the programmer and the appropriate
	menu selection. Next type ^C. This will cause an exit from the program.
	Now type DDT.COM. This will invoke DDT.COM into action. Next use DDT to
	move the data at 4000 hex down to 0100 hex. After moving the eprom data
	from 4000 hex to 0100 hex type ^C and use the SAVE command to put the
	eprom image on disk.

		EXAMPLE:

		    DDT
		    M4000,5000,0100
		    ^C
		    SAVE XX EPROM.COM
			XX depends on the size of the eprom read
			2708 XX = 4
			2716 XX = 8
			2732 XX = 16