Disk 4 documentation


There are three CP/M customizations on this disk especially for the
Big Board. See the appropriate .DOC and .LET files for step by step
instructions for incorporating into your own CP/M. In fact, if you read
ZCPR.LET you'll no doubt want to follow with a thorough look through
ZCPR.DOC.

CBIOS.HEX .DOC .Z80 .PRN
      
	This is a much needed CBIOS to support the Tandon half-wide drives.
	The problem with the Tandons is they turn themselves off rather than
	waiting for the Big Board to turn them off. So the Big Board may not
	have timed out but the Tandons have already shut down. 
	So the Big board generates an error message. See the .doc file
	written by Bob Edison.
	
	This CBIOS also supports a parallel printer. And, it looks like it
	was written for the Crowe assembler.

  Robert Edison
  Kronos Inc
  355 Western Ave
  Toston MA 02135

	
ZCPR11.HEX .ASM .DOC
	
	There are two ZCPRs on this disk. Version 1.1 (ZCPR11) is the updated
	version (see the .asm file) and was configured and assembled  by Gary
	Kaufman for those folks who got their CP/M already configured
	from DRC. You have a 59.5K CP/M (even though it says 60K on the
	screen). The base of your CCP is a D200.
	
	Gary Kaufman
	206 S 13th Street Apt 810
	Philadelphia, PA 19107
	213-735-2841
  
	
ZCPR.HEX .ASM .DOC

	Version 1 (ZCPR) is the original version and was configured by
	Gordon Banks MD for folks with the full 60K CP/M. This is for you
	if your CCP begins at D400.

	Dr Gordon banks MD
	1360 Scaife Hall
	University of Pittsburgh
	Pittsburgh, PA 15261


ZCPR1.HEX

	This is also Version 1 and also from Gordon Banks but this
	one automatically begins running whatever you have named
	STARTUP.COM. This could be BASIC, or a word processor etc.
	This doesn't work for something that does its thing and
	then immediately does a cold boot (G0000). Cold boots 
	just dump you right back into whatever is STARTUP.COM.

ZCPRBLOC.COM .ASM
	
	If you have any doubt about the base of your CCP, run ZCPRBLOC.COM.
	It will tell you. Gary Kaufman sent this.