ZCPR - A Z80 Replacement for the CP/M CC



               Documentation on ZCPR - A Z80 Replacement for the CP/M CCP

                      ZCPR is a Group Project By the CCP-GROUP:
                    RLC - Richard Conn            FJW - Frank Wancho
                    KBP - Keith Peterson          RGF - Ron Fowler


                              ZCPR Documentation By RLC


                                  Table of Contents
                                  ----- -- --------

               Introduction                                       2

               Part A: Installation Instructions                  4
                    ZCPR Integration Example                      5
                    Setting the ZCPR Inline Options               8
                      REL, BASE, CPRLOC, RAS, SUBA, CLEVEL3       8
                    Customizatioî Symboló                         9
                      NLINES, WIDE, PGDFLT, PGDFLG, MAXUSR, 
                        SFLG, SOFLG, SUPRES                       9
                      DEFUSR, SPRMPT, CPRMPT, NUMBASE,         
                        SECTFLG, FENCE                           10
                    Patching SUBMIT.COM                          11

               Part B: Usage Instructions and Explanation of
                       Commands                                  12
                    The ZCPR Command Hierarchy Search            12
                    The ZCPR-Resident Commands                   15
                      DIR, ERA                                   15
                      LIST, TYPE, SAVE                           16
                      REN, USER, DFU, JUMP                       17
                      GO, GET                                    18
                    ZCPR Error Messages                          19

               Part C: ZCPR Command Levels and How to Use Them   20













Š




                                      Page  1





                     ZCPR - A Z80 Replacement for the CP/M CC


               ZCPR is a replacement for the CP/M Console Command Processor 
          (CCP)  which  is  designed to run as part of  CP/M  on  Z80-based 
          microcomputers.   In most cases it is upward-compatible with  the 
          original CP/M Version 2.2 CCP.

               ZCPR,  however,  provides  many extensions to the CP/M  CCP.  
          Included in these extensions are the following features:

                    . The TYPE function can be made to page or not page its 
          output at the user's discretion

                    .  A LIST function is available which sends its  output 
          to the CP/M LST: Device and does NOT page

                    .  The  DIR command has been extended to allow the dis-
          play of the system files or all files

                    . The ERA command now prints out the names of the files 
          it is erasing

                    .  The  current user number may be included as part  of 
          the command prompt;  if the user is under a number other than  0, 
          the prompt is of the form 'du>' (like 'A2>' or 'B10>'),  and,  if 
          the  user is under 0,  the prompt may be 'd>' or 'd0>' as per his 
          choice

                    .  The  SUBMIT facility has been changed in  two  basic 
          ways:
                         - the  prompt  changes to 'du$' or 'd$'  when  the 
          SUBMIT command is printed
                         - the $$$.SUB is executed from drive A: (note that 
          the  original  SUBMIT  problem now exists,  but the  new  SUB.COM 
          facility  corrects it);  the CCP-GROUP definition of an  Indirect 
          Command  File  now  applies,  and this  definition  is  that  any 
          sequence of commands which may be issued from the console is also 
          a  valid  sequence  of commands for execution  from  an  Indirect 
          Command File; hence, the sequence:

                              DIR
                              B:
                              DIRŠ                              A:

          may  be  issued  from either the console or an  Indirect  Command 
          File,  and the results of the execution of this sequence are  the 
          same.   Basically,  this  says  that Indirect Command  Files  are 
          upward-compatible  to the console input (but not necessarily that 
          the  contents  of an Indirect Command File may be issued  at  the 
          console without modification).








                                      Page  2





                     ZCPR - A Z80 Replacement for the CP/M CC


                    .  A command-search hierarchy is now implemented  which 
          is executed roughly as follows:
                         - the  user's command is checked against the  CPR-
          resident commands and executed immediately if a match is found
                         - failing  that,  the  current user number on  the 
          current disk is scanned for the COM file;  the COM file is loaded 
          and executed if found
                         - failing that, a default user number (initially 0 
          but  can be reset with the DFU CPR-resident command) on the  cur-
          rent disk is scanned for the COM file; the COM file is loaded and 
          executed if found
                         - finally,  failing that,  the default user number 
          on disk A:  is scanned for the COM file;  the COM file is  loaded 
          and executed if found or an error message (COMMAND?, when COMMAND 
          was the user's command name) is printed

                    .   The  numeric  argument for the SAVE command can  be 
          specified  in hexadecimal so that the user may employ the  values 
          presented by tools such as DDT exactly as they are given

                    .  A  GET  command which loads a file  at  a  specified 
          memory address and a JUMP command which "calls" the subroutine at 
          a  specified memory address have been added;  a GO command  which 
          "calls"  the  subroutine at 100H (subset of the JUMP  capability) 
          has also been added


               This  document provides the user of ZCPR with the  following 
          information:
Š                    Part A:  Installation Instructions
                    Part B:  Usage Instructions and Explanation of Commands
                    Part C:  ZCPR Command Levels and How to Use Them
























                                      Page  3





                     ZCPR - A Z80 Replacement for the CP/M CC


                                       Part A
                              Installation Instructions

               In  order to install ZCPR on a target microcomputer (must be 
          currently running CP/M 2.2), the user must know two basic things:

                    1)  Where his CCP is currently running in memory
                    2)  Where his CCP is located in the SYSGEN  image,  or, 
          for systems which don't support SYSGEN (such as P&T CP/M 2.2  for 
          the TRS-80 Model II), where his CCP is located on disk and how to 
          place the new ZCPR on top of it

               The  first question is answered relatively easily.   A  pro-
          gram,  known  as either BDOSLOC or BDLOC (for BDOS  Locator),  is 
          provided  with ZCPR.   You should assemble this program for  your 
          particular  computer (change the base ORG if you are running non-
          ORG-0 CP/M) and execute it.   Upon execution, it will provide you 
          with  the base address of (1) the BDOS and (2) the CCP  for  your 
          particular system.   BDOSLOC has worked correctly for all systems Š          tested so far,  but there is always a chance that it may NOT work 
          for some non-tested system.   For the time being,  assume that it 
          works correctly and record the starting base page address of your 
          CCP.

               The  second question is not answered nearly so  easily.   If 
          you  have  the ability to SYSGEN your system,  it is much  easier 
          (commonly) than if you do not.   You must,  after assembling  the 
          ZCPR  properly,  integrate it into the sysgen (or disk) image  of 
          CP/M.   This  can  be  done by obtaining a SYSGEN image  of  your 
          system, scanning it via a debugger such as DDT to find the offset 
          for the CCP,  reading the new CPR in on top of the old  one,  and 
          finally  running  SYSGEN again to place the resultant  system  on 
          disk.   If  you  DO NOT have SYSGEN capability,  a  Disk  Utility 
          program  is required to locate the CCP on disk and then write the 
          new  ZCPR  on  top  of the old  one.   The  net  result  of  this 
          integration  is  the placement of the new ZCPR onto disk  in  the 
          proper  place so that it will be loaded with the rest of CP/M  on 
          cold boot and executed properly.
               To find the original CCP, you typically have to locate it by 
          its appearance.   It is probably stored contiguously on disk, so, 
          once it is found, a sequential overwrite is all that is required.  
          Probability  is extremely high that it is stored contiguously  in 
          the SYSGEN image.   The CCP starts with two (2) and ONLY TWO jump 
          instructions  followed  by a buffer area (possibly containing  an 
          initial  command and/or the Digital Research  copyright  notice).  
          The  Digital  Research manuals show the CCP to reside at  address 
          980H  in the SYSGEN image,  but this may vary  with  system.   To 
          find  this image,  use DDT or some other such debugger,  load the 
          SYSGEN image you can get via SYSGEN,  and examine memory starting 
          at around 900H for the two (and ONLY two) jumps described  above.  
          If  you find an area with more than two jumps (a group of  them), 
          you  are probably looking at the BIOS and should go lower for the 
          CCP.   The  CCP will probably start on an even page or  half-page 
          address (like 900H, 980H, 1100H, etc).



                                      Page  4





                     ZCPR - A Z80 Replacement for the CP/M CC


               Now that the location of the CCP has been found, record this 
          address for later.  You are now ready for the integration of ZCPR 
          into your system.   To do this, perform the following steps using 
          the  information  of the page address of the CCP  (obtained  from 
          BDOSLOC  and  called  CPRLOC within ZCPR) and  the  SYSGEN  image 
          address of the CCP (called IMAGE for reference in this document).

                    1.  Edit  ZCPR  and set the CPRLOC equate to the  value Š          obtained from above.  Also set any flags and values as you desire 
          (see the section on ZCPR Customization below).   When  satisfied, 
          end the edit session.

                    2.   Assemble  ZCPR  with MAC  (or  equivalent).   This 
          assembler  is  required  because of the MACROs  used.   Only  the 
          resultant HEX file is required.

                    3.   Assuming that you can use SYSGEN,  obtain a SYSGEN 
          image of your current CP/M system and save it on disk.

                    4.   Load  the  SYSGEN image into memory with  DDT  (or 
          equivalent).  Once loaded, verify that the original CCP is at the 
          IMAGE  address  found above and compute  the  integration  offset 
          using the DDT H command:
                         H<IMAGE adr>,<CPRLOC adr>
          The  second number displayed gives you the OFFSET value  required 
          for step 5.

                    5.   Integrate  ZCPR into your SYSGEN image via DDT's I 
          and ROFFSET commands.  Use IZCPR.HEX (or the name of your version 
          of  ZCPR) to load the FCB and ROFFSET (where OFFSET was  computed 
          in  step 4) to load the ZCPR.HEX file into memory at  the  proper 
          location.   Check  to see that ZCPR is indeed properly loaded  by 
          examining the SYSGEN IMAGE area.

                    6.   Place the new system on disk by running SYSGEN and 
          NOT loading the system from disk (use the memory image).

               For   further  clarification  of  the  above  process,   the 
          following  is a sample terminal session which outlines the  steps 
          taken.

                              ZCPR Integration Example


          B>; Sample terminal session for integrating ZCPR
          B>sysgen
          SYSGEN VER 2.2
          SOURCE DRIVE NAME (OR RETURN TO SKIP)b
          SOURCE ON B, THEN TYPE RETURN  <-- I hit the RETURN key here
          FUNCTION COMPLETE                                /
          DESTINATION DRIVE NAME (OR RETURN TO REBOOT)  <-- and here
          B>save 44 cpm56.com      <-- We now have a SYSGEN image of CP/M
                                        to work with




                                      Page  5




Š                     ZCPR - A Z80 Replacement for the CP/M CC


          B>xdir
          XDIR   Version 2.6  User Number:   0,  Double Density
          File Attributes:  Non-System  

          Filename.Typ Size K   Filename.Typ Size K   Filename.Typ Size K
          -------- --- ------   -------- --- ------   -------- --- ------
          !TEXTWRK.-12      0   CPR     .DOC      8   EE687   .TXT      4
          CPR     .AQM     34   TFS     .HLP      6   EE687PRE.TXT      4
          CPR     .ASM     50   CONTENTS.T01      6   SW1     .TXT     10
          CPR     .BAK      4   CONTENTS.T02      4   SW2     .TXT      2
          CPM56   .COM     12   CONTENTS.T03      4
          B:  30 Entries &   22 Files --    338K Bytes Remaining
          File Data:         14 Files --    154K Bytes Displayed
          B>bdosloc      <-- Now to locate the CCP's address
          The Base Page Address of this system's BDOS is C5
          The Base Page Address of this system's CCP is  BD <-- This is it
          B>ddt cpm56.com     <-- Now to find the CCP in the SYSGEN image
          DDT VERS 2.0
          NEXT  PC
          2D00 0100
          -d900,90f      <-- Start looking around here
          0900 31 80 E7 3E 06 3C 3C FE 1B CA 00 C2 DA 11 E7 D6 1..>.<<.........
          -da00,a0f
          0A00 31 00 01 01 01 0C C5 CD 0F E4 21 00 BE 11 00 04 1.........!.....
          -db00,b0f
          0B00 31 00 01 01 01 11 C5 CD 0F E4 21 00 C0 11 00 02 1.........!.....
          -db80,b8f
          0B80 31 00 01 01 09 01 CD A8 00 21 00 D2 11 00 C2 0E 1........!......
                  -- Detail Left Out --
          -d1100         <-- I found it at 1100H; note the 2 JMP's
          1100 C3 FF BD C3 FB BD 50 10 20 20 20 20 20 20 20 20 ......P.        
          1110 20 20 20 20 20 20 20 20 00 00 00 00 00 00 00 00         ........
          1120 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
                  -- Detail Left Out --
          -^C            <-- Return to CP/M; I know that CPRLOC will be
                              BD00H and the IMAGE offset is 1100H

          B>ed cpr.asm {edit ZCPR here and place CPRLOC=BD00H}#  
                  -- Detail Left Out --

          B>mac cpr $pz sz         <-- Now to assemble the CPR
          CP/M MACRO ASSEM 2.0
          C4F0                     <-- Note that CPR MUST end before BDOS
                                        begins!
          014H USE FACTOR
          END OF ASSEMBLY





Š




                                      Page  6





                     ZCPR - A Z80 Replacement for the CP/M CC


          B>ddt cpm56.com          <-- Now to integrate!
          DDT VERS 2.0
          NEXT  PC
          2D00 0100
          -h1100,bd00              <-- Compute offset for new CPR
          CE00 5400                <-- Offset is 5400H
          -icpr.hex                <-- Init FCB
          -r5400                   <-- Read in new CPR with offset
          NEXT  PC
          2D00 0000
          -^C                      <-- Done!
          B>sysgen                 <-- Now to SYSGEN onto disk
          SYSGEN VER 2.2
          SOURCE DRIVE NAME (OR RETURN TO SKIP)   <-- Use memory image
          DESTINATION DRIVE NAME (OR RETURN TO REBOOT)b     <-- onto B:
          DESTINATION ON B, THEN TYPE RETURN
          FUNCTION COMPLETE
          DESTINATION DRIVE NAME (OR RETURN TO REBOOT) <-- Done for now

          B>




















Š















                                      Page  7





                     ZCPR - A Z80 Replacement for the CP/M CC


                           Setting the ZCPR Inline Options

               The  following  are the four basic options available to  the 
          user under ZCPR for customization of his package.

          Option Name    Function

             REL         Configures CPRLOC (CPRLOC equ 0) for integration
                         via MOVCPM rather than the DDT/SYSGEN technique
                         outlined above; set to TRUE for MOVCPM integra-
                         tion or FALSE for DDT/SYSGEN integration

             BASE        Base address of your CP/M system; standard CP/M
                         has a base of 0, but some CP/M systems (such as
                         for the TRS-80 Model I and Heath/Zenith H89/Z89)
                         start physical RAM memory at a higher address;
                         equate BASE to the starting RAM memory address of
                         your system

             CPRLOC      This is the starting address of ZCPR; set the
                         second CPRLOC equate to the address you obtain
                         from BDOSLOC

             RAS         This is an equate which masks out selected ZCPR
                         command functions for security purposes on
                         Remote Access Systems such as Bulletin Boards;
                         the masked out functions currently include
                         SAVE, ERA, REN, JUMP, GO, and GET; set RAS to TRUE
                         to mask these out or FALSE to leave them in
Š             SUBA        This is an equate which determines the drive
                         onto which ZCPR will look for an executing
                         Indirect Command File.  If the basic philosophy
                         of the Indirect Command File described above is
                         to be maintained, this symbol should be set to
                         TRUE (look on drive A: for the $$$.SUB file); if
                         not, this symbol should be set to FALSE (look on
                         the default drive from the $$$.SUB file).  To
                         review, the basic philosophy of the Indirect
                         Command File is that any sequence of commands
                         which may be issued from the console (within
                         reason, which means NOT to erase a $$$.SUB file)
                         may also be issued from within an Indirect
                         Command File, and the resultant execution should
                         be identical (same functions performed).

             CLEVEL3     This equate enables or disables extended Command
                         Level 3 Processing.  If set to TRUE, extended
                         Command Level 3 Processing is enabled and the user
                         command line is automatically capitalized, the
                         terminating zero is placed at the end of the
                         buffer, and the internal CIBPTR is set correctly
                         (see later for more information).




                                      Page  8





                     ZCPR - A Z80 Replacement for the CP/M CC


                                Customization Symbols

               The following symbols are provided for further customization 
          of ZCPR to a user's particular tastes and hardware facilities.

          Option Name    Function

             NLINES      Number of lines on the user's CRT for paging

             WIDE        This equate is used to select a narrow or wide
                         display under the DIR command; if WIDE is equated
                         to TRUE, each file name is separated by two
                         spaces, a FENCE, and two more spaces; if WIDE is
                         equated to FALSE, each file name is separated by
                         one space, a FENCE, and one more space

             PGDFLT      This is the Paging Default flag for the TYPE
                         command; if PGDFLT is set to TRUE, the TYPE
                         command will page its output by default andŠ                         the P option on the TYPE command (see below)
                         will prohibit paging; if PGDFLT is set to FALSE,
                         the TYPE command will NOT page its output by
                         default and the P option will enable paging

             PGDFLG      This sets the option character in the command
                         line for the TYPE command (the 'P' mentioned
                         above); if the user wishes to change this option
                         character, he need only change this equate

             MAXUSR      This is the largest user number recognized by
                         the USER command; if the user wishes to protect
                         the higher user areas, he may set this symbol
                         to the highest area normally accessable; 15 is
                         the largest permitted value for MAXUSR

             SYSFLG      This is the option character for the DIR command
                         line which is used to specify that DIR search
                         All Files (both $SYS and $DIR) for its display;
                         the distributed default for this is 'A'

             SOFLG       This is the option character for the DIR command
                         line which is used to specify that DIR search
                         ONLY the $SYS files for its display; the distri-
                         buted default for this is 'S'

             SUPRES      Set SUPRES to TRUE to suppress printing the user
                         number when the user is under User Number 0 or
                         set SUPRES to FALSE to ALWAYS display the User
                         Number with the CPR prompt; with SUPRES set to
                         TRUE, a user on B: in user 0 sees 'B>' as the
                         prompt, but with SUPRES set to FALSE, a user on
                         B: in user 0 sees 'B0>' as the prompt





                                      Page  9





                     ZCPR - A Z80 Replacement for the CP/M CC


             DEFUSR      This is the CPR-default user number which is
                         searched in the command hierarchy for the COM
                         files (distributed as 0); the DFU changes this
                         temporarily until a Warm Boot or Cold Boot is
                         done, at which time the search reverts to this
                         value

             SPRMPT      This is the CPR prompt character which indicatesŠ                         that a SUBMIT file is in execution; by default
                         it is set to '$', so prompts like 'A$' appear
                         during SUBMIT file execution

             CPRMPT      This is the CPR prompt character which indicates
                         that the CPR is awaiting a user console command;
                         by default it is set to '>', so prompts like
                         'A>' appear during user input to the CPR

             NUMBASE     This is the escape character used by those
                         commands which require a DECIMAL number as
                         an argument; placing this character after
                         the number argument switches the base to
                         HEXADECIMAL; for example, 'SAVE 15 MYFILE' can be
                         expressed as 'SAVE FH MYFILE' if NUMBASE is
                         set to 'H' (the default)

             SECTFLG     This character constant is the suffix option for
                         the SAVE command which specifies that sectors,
                         as opposed to pages, are to be saved; the default
                         value is 'S'

             FENCE       This is the character printed to separate entries
                         in a directory listing; it's default value is '|'

























                                      Page  10




Š                     ZCPR - A Z80 Replacement for the CP/M CC


                                 Patching SUBMIT.COM

               SUBMIT.COM  may be patched to run with ZCPR by the following 
          procedure  (this  is  recommended  if  the  user  does  not  have 
          SUB.COM).   This  patch simply makes it always place the  $$$.SUB 
          file on Drive A:.  Illustrative terminal session follows:

          A>ddt b:submit.com
          DDT VERS 2.0
          NEXT  PC
          0600 0100
          -s5bb           <-- Patch is at 5BB Hex
          05BB 00 1       <-- Change 0 (default drive) to 1 (drive A:)
          05BC 24 .       <-- That's it!
          -d5b0 5cf       <-- See change
          05B0 00 00 00 00 00 00 30 30 31 20 24 01 24 24 24 20 ......001 $.$$$ 
          05C0 20 20 20 20 53 55 42 00 00 00 1A 1A 1A 1A 1A 1A     SUB.........
          -^C             <-- Done
          A>save 5 newsubmt.com   <-- Save new SUBMIT.COM file
































Š




                                      Page  11





                     ZCPR - A Z80 Replacement for the CP/M CC


                                      Part B
                   Usage Instructions and Explanation of Commands


               The  following instructions are written with the  assumption 
          that  the  reader is quite familiar with how to use CP/M 2.2  and 
          its CCP.   ZCPR is written as a logical extension of the CP/M 2.2 
          CCP philosophy and should be addressed as such.



                          The ZCPR Command Hierarchy Search

               The first,  and most basic thing, to learn about ZCPR is the 
          order in which is searches for a COM file for execution or a file 
          specified  by the GET command.   Under the CP/M 2.2 CCP,  if  the 
          specified  COM file command was not found on the current drive in 
          the  current user area,  the CCP aborted with an  error  message.  
          ZCPR,  however,  continues searching from this point a maximum of 
          two  more  levels.   This command hierarchy search  was  outlined 
          above and is described here in further detail.

                    1.   If  the  command is of the form 'COMMAND' and  NOT 
          'd:COMMAND',  the  CPR-resident  command list is searched  for  a 
          match.   If  the  match is found,  the  CPR-resident  command  is 
          immediately processed.   If the match is not found or the command 
          is  of the form 'd:COMMAND',  the next step is taken.   Note that 
          the  'd:COMMAND'  form is good for executing a command  COM  file 
          which  has the same name as a CPR-resident command (such as  SAVE 
          or DIR).

                    2.   If  the command is of the form  'd:COMMAND',  disk 
          drive  'd:'  is  temporarily logged in for  the  purpose  of  the 
          command  search.   Otherwise,  the  currently logged-in drive  is 
          used.

                    3.  Now the file named COMMAND.COM is searched for.  If 
          found,  it  is loaded into memory starting at 100H and  executed.  
          If not, proceed to step 4.

                    4.   Now  that  the first search  for  COMMAND.COM  has Š          failed,  the  CPR checks to see if the user is under the  current 
          Default User Number.   The Default User Number may be that set by 
          the  DEFUSR equate in the CPR or that set by the user via the DFU 
          command.   DEFUSR  is in effect if DFU has not been issued  since 
          the last Warm or Cold Boot, and DFU is in effect if it was issued 
          since the last Warm or Cold Boot.   If the user is NOT under  the 
          current  Default User Number,  ZCPR temporarily logs him into  it 
          and  searches  the directory.   If COMMAND.COM is  found,  it  is 
          loaded as described above and executed.  If not, ZCPR proceeds to 
          the next step.






                                      Page  12





                     ZCPR - A Z80 Replacement for the CP/M CC


                    5.   The user is now in the Default User Number, and at 
          this  point,  ZCPR checks to see if the user is on disk drive A:.  
          If not, it temporarily logs into A: and searches the default user 
          number  of  A:  for  COMMAND.COM.   If found,  it  is  loaded  as 
          described above and executed.   If not,  ZCPR prints the  command 
          name  as  an  error message and returns to  command  input  mode, 
          aborting the SUBMIT file if COMMAND came from it.

               In  all cases of the search above,  if COMMAND.COM is found, 
          after  it  is loaded into memory,  ZCPR resets the  user  to  his 
          original disk drive and user number.  Hence, the files referenced 
          by the user by default are obtained from this environment.

               To  illustrate this command hierarchy search,  consider  the 
          following examples:

          Example 1:  DEFUSR equ 0 {default user number is 0}

          B10>           <-- User is on Drive B:, User Number 10
          B10>ASM TEST.BBZ    <-- User wishes to assemble TEST.ASM in
                                   Drive B:, User 10
               <-- At this point, ZCPR looks on B:/10 for ASM.COM, fails,
                    looks on B:/0, fails, and finally looks on A:/0; it
                    finds ASM.COM here and goes back to B:/10 for the file


          Example 2:  DEFUSR equ 0 and DFU issued

          B10>           <-- User is on Drive B:, User Number 10
          B10>DFU 5      <-- User Selects User 5 as defaultŠ          B10>ASM TEST.BBZ    <-- As above
               <-- At this point, ZCPR looks on B:/10 for ASM.COM, fails,
                    look on B:/5, fails, and finally looks on A:/5; it
                    fails here also and prints ASM? as an error message

          Example 3:  DEFUSR equ 0

          B>             <-- User is on Drive B:, User Number 0
          B>ASM TEST.BBZ      <-- As above
               <-- At this point, ZCPR looks on B:/0 for ASM.COM, fails,
                    looks on A:/0, fails, and prints error message

          Example 4:  DEFUSR equ 0

          A10>           <-- User is on Drive A:, User Number 10
          A10>ASM TEST.AAZ    <-- As above, but file on A:
               <-- At this point, ZCPR looks on A:/10 for ASM.COM, fails,
                    looks on A:/0, fails, and prints error message









                                      Page  13





                     ZCPR - A Z80 Replacement for the CP/M CC


          Another Example:

                    For  example,  if the user is logged into Drive  B:  in 
          User Area 10, the Default User Number is 0, and the following COM 
          files are present as indicated --

                         WM.COM on Drive A: in User 0
                         MBASIC.COM on Drive A: in User 0 and on
                              Drive B: in User 0
                         TEST.COM on Drive B: in User 10 and Drive B:
                              in User 0

          then  the  following  happens when  the  following  commands  are 
          issued from the console (or Indirect Command File):

          B10>WM TEST2.TXT
           \   \    \__ File to be edited
            \   \__ Invoke the WM.COM file (Word Master editor)
             \__ User is on Drive B: in User Area 10Š
               Results:
                    ZCPR searches B:  User 10, B: User 0, and A: User 0 for 
          WM.COM;  it finds WM.COM in A:  User 0,  loads it,  logs the user 
          back into B: User 10, and executes it.

          B10>MBASIC
           \    \__ Invoke the MBASIC.COM file (MBASIC Interpreter)
            \__ User is on Drive B: in User Area 10

               Results:
                    ZCPR searches B:  User 10 and B: User 0 for MBASIC.COM; 
          it finds MBASIC.COM in B: User 0, so it doesn't bother to look on 
          A:  User 0.   MBASIC.COM is then loaded and executed as described 
          in the previous example.

          B10>TEST
            \   \__ Invoke the TEST.COM file (TEST program)
             \__ User is on Drive B: in User Area 10

               Results:
                    ZCPR  searches  B:  User  10  for  TEST.COM;  it  finds 
          TEST.COM in B:  User 0,  so it doesn't bother to look further (if 
          it had,  it would have found TEST.COM in B: User 0).  TEST.COM is 
          then loaded and executed as described above.

          B10>TEST2
            \    \__ Invoke the TEST2.COM file (TEST2 program)
             \__ User is on Drive B: in User Area 10

               Results:
                    ZCPR searches B:  User 10, B: User 0, and A: User 0 for 
          TEST2.COM;  it  doesn't find it,  so it issues the error  message 
          'TEST2?', which says it couldn't find TEST2.COM.




                                      Page  14





                     ZCPR - A Z80 Replacement for the CP/M CC


                             The ZCPR-Resident Commands

               The  following  pages describe the  ZCPR-Resident  Commands.  
          These  are commands located within ZCPR itself which are executed 
          from within ZCPR.  The phrases <afn> and <ufn> refer to ambiguous 
          file name and unambigous file name as per the CP/M convention.

          Command: DIRŠ          Function:  To Display a listing of the names of the files on disk
          Forms:
               DIR <afn>           <-- Displays $DIR files
               DIR <afn> S         <-- Displays $SYS files
               DIR <afn> A         <-- Displays both $DIR and $SYS files
          Customization Variables:
               WIDE      SYSFLG    SOFLG     FENCE
          Examples:
               DIR *.ASM           <-- All $DIR .ASM files
               DIR *.COM S         <-- All $SYS .COM files
               DIR *.COM A         <-- All .COM files
          Notes:
               If  a  file is scanned for and no such name exists on  disk, 
          the  'No  Files' message will appear.   However,  if  a  file  is 
          scanned for and the name exists as a $SYS file and $DIR files are 
          being  scanned for,  no file name is displayed but the 'No Files' 
          message does NOT appear.  For example, if TEST.COM is a $SYS file 
          and  'DIR  TEST.COM' is issued,  no  message  appears.   If  'DIR 
          TEXT.COM' is issued and TEXT.COM does not exist on disk,  the 'No 
          Files' message is displayed.


          Command: ERA
          Function:  To Erase the specified $R/W files from disk
          Forms:
               ERA <afn>           <-- Erase both $DIR and $SYS files
          Customization Variables:
               WIDE      FENCE
          Examples:
               ERA *.ASM           <-- Erase all .ASM files
               ERA *.*             <-- Erase all files
          Notes:
               If a $R/O file is encountered,  a BDOS error message will be 
          displayed  and the procedure is stopped.   The user is unsure  at 
          this  time as to which files have been erased and which have  not 
          and should check.  Sorry for this problem!  The ERASE command (to 
          be  given  to SIG/M by RLC in the near future) is a  solution  to 
          this problem.











                                      Page  15




Š                     ZCPR - A Z80 Replacement for the CP/M CC


          Command: LIST
          Function:  To Print the specified file on the CP/M LST: device
          Forms:
               LIST <ufn>          <-- Print the file (no paging)
          Customization Variables:
               -None-
          Examples:
               LIST TEST.TXT       <-- Print TEST.TXT on LST:
          Notes:
               If  the file has a $SYS attribute,  it will be found as well 
          as those with $DIR attributes.


          Command: TYPE
          Function:  To Print the specified file on the CP/M CON: device
          Forms:
               TYPE <ufn>          <-- Print the file with the paging deflt
               TYPE <ufn> P        <-- Print the file with the paging deflt
                                        negated
          Customization Variables:
               NLINES    PGDFLT    PGDFLG
          Examples:
               TYPE TEST.TXT
               TYPE TEST.TXT P
          Notes:
               When  the  display pauses during paging,  type any  char  to 
          continue or ^C to abort.  ^S also works.


          Command: SAVE
          Function:  To Copy the TPA starting at 100H to disk
          Forms:
               SAVE <Number of Pages> <ufn>  <-- <Number of Pages> in DEC
               SAVE <Number of Pages>H <ufn> <-- <Number of Pages> in HEX
               SAVE <Number of Sectors> <ufn> S  <-- Number of sectors
               SAVE <Number of Sectors>H <ufn> S <-- Number of sectors
          Customization Variables:
               NUMBASE   RAS
          Examples:
               SAVE 15 MYFILE.TXT        <-- 15 pages saved
               SAVE FH MYFILE.TXT        <-- 15 pages saved
               SAVE 10H MYFILE.TXT S     <-- 16 sectors (8 pages) saved
          Notes:
               If the file name to be saved already exists,  then SAVE will 
          exit with the message 'Delete File?'; if the user REALLY wants to 
          save  under  this name,  he may then type Y or y and the  current 
          file will be deleted and then recreated containing the  specified 
          part of the TPA.



Š




                                      Page  16





                     ZCPR - A Z80 Replacement for the CP/M CC


          Command: REN
          Function:  To Change the name of a disk file
          Forms:
               REN <ufn new>=<ufn old>
          Customization Variables:
               RAS
          Examples:
               REN NEWFILE.TXT=OLDFILE.TXT
          Notes:
               If <ufn new> already exists, the message 'Delete File?' will 
          be  printed  and the user may respond with Y or y to  delete  the 
          current <ufn new> and then rename <ufn old> to <ufn new>.

          Command: USER
          Function:  To Change the current user number
          Forms:
               USER <User Number>       <-- <User Number> in DEC
               USER <User Number>H      <-- <User Number> in HEX
          Customization Variables:
               -None-
          Examples:
               USER 15        USER FH        USER 0
               USER      <-- Same as USER 0
          Notes:
               -None-


          Command: DFU
          Function:  To Temporarily Change the default user number for the
                     command hierarchy search
          Forms:
               DFU <User Number>        <-- <User Number> in DEC
               DFU <User Number>H       <-- <User Number> in HEX
          Customization Variables:
               -None-
          Examples:
               DFU 15         DFU FH         DFU 0
               DFU       <-- Same as DFU 0
          Notes:
               See above for explanation.
Š
          Command: JUMP
          Function:  To "call" the subroutine at the specified page address
          Forms:
               JUMP <Address> <Cmd Parms> <-- <Address> in HEX
          Customization Variables:
               NUMBASE   RAS
          Examples:
               JUMP E000 or JUMP E000H  <-- Jump to E000H
               JUMP                     <-- Jump to 000H
               JUMP 0                   <-- Jump to 000H
          Notes:
               JUMP performs a subroutine "call", so the called routine may 
          return to the ZCPR by either a RET or a Warm Boot.


                                      Page  17





                     ZCPR - A Z80 Replacement for the CP/M CC


          Command: GO
          Function:  To "call" the subroutine starting at 100H
          Forms:
               GO <Cmd Parms>           <-- Execute reentrant at 100H
          Customization Variables:
               RAS
          Examples:
               GO *.ASM                 <-- Assuming XDIR is loaded,
                                             gives directory of *.ASM
          Notes:
               This  command is identical in function to JUMP  100H;  JUMP, 
          however, leaves the address as the first entry in CP/M BASE + 80H 
          (the input line buffer), while GO has no such address.


          Command: GET
          Function:  To load a file from disk into memory starting at the
                     specified page
          Forms:
               GET <Address> <ufn>      <-- <Address> in HEX
          Customization Variables:
               NUMBASE   RAS
          Examples:
               GET 8000 TEST.80         <-- Load TEST.80 starting at 8000H
               GET 100 TEST.80 or GET 100H TEST.80 <-- Load TEST.80      
                                             starting at 100H
               GET 0 TEST.80            <-- Load TEST.80 starting at 000H
          Notes:
               GET  searches for the specified file according to  the  same 
          command  hierarchy  search employed by the ZCPR command  scanner.  Š          Hence,  if the user is on B:/10 and the file is on A:/0 with  the 
          current  default user number at 0,  GET will search from B:/10 to 
          B:/0 to A:/0 in looking for the file.
























                                      Page  18





                     ZCPR - A Z80 Replacement for the CP/M CC


                                 ZCPR Error Messages

               The  following  are the error messages issued  by  ZCPR  and 
          their meanings.

          Message   Meaning

          ?         Printed after a command or an argument means that such
                      was invalid

          No File   From DIR, this means that DIR did not locate any files
                    Also from ERA with the same meaning

          All?      Issued in response ERA *.*, asks the user is he really
                      wants to erase all the files.  Unlike under the
                      original CP/M 2.2 CCP, single character input is
                      required (Y or y for yes and anything else for no)
                      with NO <CR> to end the line
Š          Full      From SAVE, means that there is not enough space on
                      disk
                    From GET or command load by CPR, means that there
                      is not enough space in memory

          Delete File?
                    From REN or SAVE, means that the file specified already 
                      exists on disk and the user may type Y or y to delete 
                      it and proceed with the REN or SAVE function





























                                      Page  19





                     ZCPR - A Z80 Replacement for the CP/M CC


                                       Part C
                       ZCPR Command Levels and How to Use Them


               ZCPR  Version 1.0 and beyond supports three distinct command 
          levels in its implementation.  Each level constitutes a different 
          way to issue a command for ZCPR to process.
Š               Command Levels 1 and 2 are common to all implementations  of 
          CP/M  and CP/ZM from CP/M Version 1.4.   Command Level 1 is  that 
          command level in which the command is issued by the user from his 
          console  terminal.   The  prompt  'd>' or 'du>'  appears  on  the 
          terminal,  and  the  user  is allowed to enter the  command  with 
          editing from the terminal.  Command Level 2 is that command level 
          in which the command is entered from an executing $$$.SUB file.

               In  both cases,  the command is stored in the internal  ZCPR 
          buffer called CIBUFF (Command Input BUFFer).   Under both Command 
          Levels  1  and 2,  the command is placed into  this  buffer,  the 
          characters of the command line are capitalized, a character count 
          which  indicates the number of characters in the command line  is 
          stored in CBUFF (the byte before CIBUFF),  an ending binary 0  is 
          placed  after  the last character in the command  line,  and  the 
          internal  pointer CIBPTR (Command Input Buffer PoinTeR) is set to 
          point to CIBUFF (the first character of the command line).

               Command  Level 3 is an extended concept to Command Levels  1 
          and  2  which is specifically supported by ZCPR Version  1.0  and 
          beyond.  This command level allows a transient program to place a 
          command  line into CIBUFF and the character count into CBUFF  and 
          have this command line executed by ZCPR.   Once control is trans-
          ferred to ZCPR to execute the command line, the transient program 
          which  placed  the command line loses control and the command  is 
          executed  exactly as though it had been typed by the user at  his 
          console terminal.

               In  order  for  a transient program to utilize  the  Command 
          Level 3 facility, this program MUST do the following:

                    1.  Locate the ZCPR.  Since the ZCPR is ALWAYS 2K bytes 
          in  size and located directly under the BDOS,  the transient  can 
          locate  the  ZCPR  by examining the BDOS entry  page  address  at 
          location  7  and  subtracting 8 from this number (8  pages  =  2K 
          bytes).  The resulting number is the base page address of ZCPR.

                    2.   Store the command line in CIBUFF and the character 
          count  in  CBUFF.   Knowing the base page address  of  ZCPR,  the 
          following information is useful in doing this:









                                      Page  20




Š                     ZCPR - A Z80 Replacement for the CP/M CC


                         ORG  CPRLOC    ;Base Address of ZCPR
                         JMP  CPR       ;Enter ZCPR and Execute Default Cmd
                         JMP  CPR1      ;Enter ZCPR and Don't Execute
               MBUFF:    DB   BUFLEN    ;Size of CIBUFF in bytes
               CBUFF:    DS   1         ;Number of Bytes in Command Line
               CIBUFF:   DS   BUFLEN    ;Buffer for Command Line
                         DS   1         ;Buffer for Ending 0 (set by ZCPR)
               CIBPTR:   DS   2         ;Address of CIBUFF (set by ZCPR)


                    3.   Obtain  the User/Disk Flag.   Location 4  contains 
          this number,  but the user may select a flag of his choice.  This 
          flag  is  one  byte  long,  and the high-order  nybble  (4  bits) 
          contains  the user number and the low-order nybble  contains  the 
          disk  number to process the command from.   The User/Disk Flag is 
          to be passed to ZCPR in the C Register.

                    4.  When ready, transfer control to ZCPR to process the 
          command by JMPing to the base address of ZCPR.   The first JMP in 
          the JMP Table given above is at this address.  At this time, ZCPR 
          will  log in the user and disk in the User/Disk Flag and  process 
          the Command Level 3 Command Line.





























Š




                                      Page  21





                     ZCPR - A Z80 Replacement for the CP/M CC


               The  following  is a sample program  which  illustrates  the 
          steps outlined above:

          ;
          ;  Demonstration of Command Level 3 Facility by RLC
          ;
          udflag  equ     4       ;Address of User/Disk Flag
          bdos    equ     5       ;Address of BDOS Entry Point

                  org     100h

                  lxi     d,prmpt ;Print User Prompt
                  mvi     c,9     ;PRINT function
                  call    bdos

                  lhld    bdos+1  ;Get address of BDOS
                  mov     a,h     ;High-Order Address in A
                  sui     8       ;A=High-Order Address of CPR
                  mov     h,a     ;HL=Address of CPR
                  mvi     l,0
                  shld    cpr     ;Save address in buffer

                  lxi     d,6     ;Point to command line buffer
                  dad     d       ;HL points to command line buffer
                  xchg            ;DE points to command line buffer
                  mvi     c,10    ;READLN into this buffer
                  call    bdos

                  lhld    cpr     ;Get Address of CPR
                  lda     udflag  ;Get User/Disk Flag
                  mov     c,a     ; ... in C
                  pchl            ;Run Command Line

          cpr:    ds      2       ;CPR Address buffer
          prmpt:  db      'User Command? $'

               Enjoy using ZCPR!
                                        -- RLC


Š















                                      Page  22