NULU MODIFICATION

This  is an update to Martins original documentation.  It details
which locations to patch to install NULU. These have been updated
as part of the modification process to create NULU 1.52.

Patches are listed in the order in which they appear in NULU.COM.
Each  patch  is  explained  and the  default  values  are  listed
immediately  next  to  the  patch  address.   All  addresses  are
absolute hexadecimal.

Patch     Default             Explanation
00194h      50h               Number  of  characters  each   full
                              video   line  can   contain.    Not
                              necessarily  the same as the number
                              you can see.
00195h      50h               Number  of characters visible on  a
                              line at any one time.
00198h      07h               This  byte indicates the number  of
                              files  that NULU can have  open  at
                              any  one time.   The base number is
                              4 and should never fall below that.
                              The value of 3 has been added to it
                              to  allow  3 level nesting  of  NCF
                              files.    If   the  NCF  value   is
                              increased or  decreased,  identical
                              changes  should  be  made  to  this
                              byte.  (See Patch at 00251h.)
00199h   0010h                This   obscure  word  controls  the
                              number  of relocatable  tasks  that
                              can   be  controlled  by  the  NULU
                              memory     management     routines.
                              Because each file is a  relocatable
                              task,  the  same modifications  for
                              the previous byte apply here.   The
                              base  value  of this word is  000dh
                              and  should never fall  below  that
                              point.  (See Patch at 00251h.)
0019bh     10h                Number  of  contiguously   numbered
                              disk drives in your system.  If you
                              have drives A and B, set this value
                              to  2.   It  will prevent you  from
                              accessing an invalid drive.
0019ch     10h                Number  of  contiguous  user  areas
                              that   NULU  will  be  allowed   to
                              access.   Under  normal  CP/M  2.2,
                              Turbo-Dos  or  a  ZCPR  system,   I
                              understand that this number can  be
                              as high as 20h.   For CP/M Plus  or
                              most  systems  that  use  time/date
                              stamping  this  number  should  not
                              exceed 10h.
001cdh    0005h               This  is  the address of  the  BDOS
                              vector.  All operating system calls
                              go  through this address.   If  you
                              have some weird,  non-standard CP/M
                              implementation  you can patch  this
                              to try to make NULU work with it.

0024dh      00h               Set  to  a non-zero value  to  make
                              NULU READ/ONLY.   No operators will
                              be  executed that could change  the
                              library or disk directories in  any
                              way.
0024eh      00h               LU.COM   was   set   up   to   exit
                              automatically if a command tail was
                              used when LU was invoked.  With the
                              release  version of NULU,  it takes
                              the -X command to exit.   Set  this
                              byte to a 01h to get it to act like
                              LU  in this respect.   That is,  it
                              will   automatically   exit   after
                              executing the passed command  tail,
                              if one was present.
0024fh      01h               Set  to  a 00h to start  NULU  with
                              BRIEF  mode  ON (long messages  not
                              printed).
00250h      01h               Set  to zero to prevent users  from
                              being  able  to  ESC,RET  from  the
                              PROMPT  AND CHAIN TO PREVIOUS  MODE
                              prompts in NCF files.  (Be sure  to
                              also  change  the values at  00198h
                              and 00199h.)
00251h      03h               This  byte  indicates  the  nesting
                              level  allowed  for NCF  files.   I
                              have  no idea what the upper  limit
                              is,  but  watch  that  Data  Buffer
                              Size!
00252h      '-Y *LBR -O',0    Starting here are 39 bytes in which
                              any  valid  NULU operators  may  be
                              stored.     This   line   will   be
                              automatically executed when NULU is
                              loaded,   even  before  any   other
                              parameters  passed  on the  command
                              line.  This might be used to create
                              a  version  of  NULU  that,   after
                              loading,    sets   the   drive/user
                              defaults to B0:,  prints the  menu,
                              scans  the drive for library files,
                              then  switches to the open  library
                              mode.  That command line would look
                              like this:

                              -U B: -H -Y *LBR -O

                              Notice that all characters in  this
                              line  MUST  be  UPPER  CASE.    The
                              entire line MUST be terminated by a
                              null  byte.    Only  39  bytes  are
                              available  for  text...not  a  byte
                              more.   The  40th  byte is for  the
                              null terminator.


002a0h      3ch               This  is  the number of lines  that
                              NULU will print on each page during
                              member file printing.   Change this
                              value  in accordance with the  line
                              printer  patch  below.   Set it  to
                              zero  to  have  NULU  ignore   line
                              counts altogether.

Starting at 0027dh are 5 data areas used to define strings needed
to control the console attributes.  Each string is preceded by an
identification  byte  and a byte indicating  its  active  length.
Then 5 bytes are available for the actual definition.   Therefore
a  total  of 7 bytes is consumed for  each  video  control.   The
attributes are, in order:
     DIM or REVERSE VIDEO ON   (DIM is preferred)
     DIM or REVERSE VIDEO OFF
     UNDERLINING ON
     UNDERLINING OFF
     CLEAR SCREEN

Each control becomes active as soon as it is patched in.

Likewise,  there  is one string defined for the LST:  device that
will be issued immediately before printing a file.   It begins at
002a2h and has the same format as the strings above.