Notes on using AMS.LIB and AMLOAD.COM

AMS.LIB is an experimental library for use with Small C to allow programs
to be run under the Amstrad AMSDOS operating system. It includes the
essential run-time routines in CRUN2.LIB, some very basic console I/O
functions and also some simple graphical colour changing and plotting
routines. The numerical routines in NUMIO2.LIB can be #included after
it if needed. Command line arguments are NOT supported.

The #define statements at the beginning of the library are used to
save having to keep looking up colour values. If you don't like
them change them!

No ORG statement is included in the library so a program intended for
AMSDOS should start with:
#asm
 ORG 4000H ; (or whatever the start address is to be)
#endasm
#include <ams.lib>
.. rest of program
If you are happy to always start your machine code files at the same
address you could put the ORG into the library.

After compiling the program the program should be assembled with ZSM or
Z80ASM to generate a HEX file.
The HEX file should then be loaded with AMLOAD.COM using the command:
AMLOAD filename     (no type .HEX needed)
The BIN file produced can then be run under AMSDOS with the usual
command:  RUN "filename"

AMLOAD can be used with HEX files produced with ordinary assembler
language programs. The machine code is built up in memory before
it is saved to disk so the programs should not be too enormous.

The routines were developed on a CPC464 under CP/M 2.2, I don't know
if there will be any problems on other Amstrad CPC's. The addresses in
the library are those given in the CPC464 Firmware Specification and
there is a great deal of scope for further modification by anyone with
a copy of that manual, sound routines are an obvious extension.

Routines in AMS.LIB

getp()		Get byte from port. No handshaking etc.
putp(ch)	Send byte to a port.
getchar()	Get byte value from keyboard - no cursor
cgetchar()	Get a byte from keyboard with cursor
putchar(ch)	Send byte to screen
puts(ptr)	Send null terminated string pointed to by ptr to screen
		\n is supported to give a new line
gets(ptr)	Get a null terminated string into a buffer pointed to
		by ptr. Up to 40 chars allowed.
crlf()		Send CR/LF to screen
plot(x,y)	Plot point at x,y
border(colour)	Set border to colour given by arg value
ink(ink_no,col)	Set colour to be used for an ink no
mode(no)	Set screen mode
paper(ink_no)	Set paper colour for text 
gpaper(ink_no)	.................... graphics
cls()		Clear screen to ink 0
gcls()		Clear graphics window
tcls()		Clear current text window
stream(n)	Select text stream
window(row1,row2,col1,col2) Set up text window
twink(ink_no,colour1,colour2) Set alternating coloured ink
locate(row,col)	Locate text cursor
transp()	Set transparent text mode
opaque()	... opaque     ........
pen(ink_no)	Choose ink to be used for text and graphics
curon()		Turn on cursor
curoff()	Turn off cursor
line(x1,y1,x2,y2) Draw line from x1,y1 to x2,y2
join(x1,y1,x2,y2,x3,y3,....xn,yn,n) join up any number of points. The
		number of points to be joined must follow the pairs of
		coordinates.
go_on(x,y)	Continue line to point x,y
rand(n)		Generate a random number between 0 and n. n can be 
		negative. If n is 0 the number will lie within +/-32k.

			J.M.H.Hill   (Dec 1985)
ÍÓÍéÌÊmÒÍÓÍÍÃ†ÓÍêÏÃ†ÓÍfÐÃ	Î‚ÒÍ§ÌÃ†ÓFILE EXISTSÍøÏþÒ	Î_:ÎÓþ Ê	ÎÍÍÃ‰ÓÍõÍ:ÎÓþ ÂÄÒ:ðÓ·Ê‰Ó=2