FU12 TERMINAL INSTALLATION           page 1 of 5
     
     Since FU12 uses a full screen display, efficient operation of 
screen functions (scrolling, and positioning to a different place in 
the file) depend on the following terminal functions:

          Erase to end of line 
          Insert a line
          Delete a line

     If your terminal does not support these functions, they will be 
supplied by FU12, however, screen updates will be much slower since the 
entire screen must be re-written.

     Before you use FU12.COM, it must be installed to your particular 
terminal, i.e. provided with information regarding control characters 
required for certain functions.  This installation is easily performed 
using the program FUINST.COM which is described in the following.
[AMSTRAD PCW users: Installation has been completed for the version
on this disc. You only need the installation program if you want to
use a different computer.]

     After having made a work-copy, please store your distribution 
diskette safely away and work only on the copy.

     Now start the installation by typing FUINST.COM at your terminal.  
Select Screen installation from the main menu.  

Installation

     A menu listing a number of popular terminals will appear, 
inviting you to choose one by entering its number:

------------------------------------------------------------------
   Choose one of the following terminals:

     1) ADDS 20/25/30          15) Lear-Siegler ADM-31    
     2) ADDS 40/60             16) Liberty                
     3) ADDS Viewpoint-1A      17) Morrow MDT-20          
     4) ADM 3A                 18) Otrona Attache         
     5) Ampex D80              19) Qume                   
     6) ANSI                   20) Soroc IQ-120           
     7) Apple/graphics         21) Soroc new models       
     8) Hazeltine 1500         22) Teletext 3000          
     9) Hazeltine Esprit       23) Televideo 912/920/925  
    10) IBM PC CCP/M b/w       24) Visual 200             
    11) IBM PC CCP/M color     25) Wyse WY-100/200/300    
    12) Kaypro 10              26) Zenith                 
    13) Kaypro II and 4        27) None of the above      
    14) Lear-Siegler ADM-20    28) Delete a definition    

   Which terminal? (Enter no. or ^X to exit):
------------------------------------------------------------------
                    Terminal Installation Menu

                                                          page 2 of 5

     If your terminal is mentioned, just enter the corresponding 
number, and the installation is complete.  Before installation is 
actually performed, you are asked the question:

------------------------------------------------------------------
   Do you want to modify the definition before installation?
------------------------------------------------------------------

     This allows you to modify one or more of the values being 
installed as described in the following.  If you do not want to modify 
the terminal definition, just type N, and the installation completes 
by asking you the operating frequency of your CPU (see last item in 
this file).

     If your terminal is not on the menu, however, you must define the 
required values yourself.  The values can most probably be found in 
the manual supplied with your terminal.

     Enter the number corresponding to None of the above and answer 
the questions one by one as they appear on the screen.

     In the following, each command you may install is described in 
detail.  Your terminal may not support all the commands that can be 
installed.  If so, just pass the command not needed by typing RETURN 
in response to the prompt.  If Delete line, Insert line, or Erase to 
end of line is not installed, these functions will be emulated in 
software, slowing screen performance somewhat.

     Commands may be entered either simply by pressing the appropriate 
keys or by entering the decimal or hexadecimal ASCII value of the 
command.   If a command requires the two characters 'ESCAPE' and '=', 
you may:

either Press  first  the Esc key,  then the =.   The entry will  be 
       echoed with appropriate labels, i.e.  <ESC> =.

or     Enter  the  decimal  or  hexadecimal  values  separated  by 
       spaces.   Hexadecimal  values must be preceded by a  dollar-
       sign.   Enter e.g.  27 61  or  $1B 61  or  $1B $3D  which are 
       all equivalent.  

     The two methods CANNOT be mixed, i.e. once you have entered a 
non-numeric character, the rest of that command must be defined in 
that mode, and vise versa.  

     A hyphen entered as the very first character is used to delete a 
command, and echoes the text Nothing.

Terminal type:

          Enter the name of the terminal you are about to install.  
     When you complete FUINSTAL.DOC, the values will be stored, and 
     the terminal name will appear on the initial list of terminals.  
     If you later need to re-install FU.COM to this terminal, you can 
     do that by choosing it from the list.  

Send an initialization string to the terminal?

          If you want to initialize your terminal when FU.COM starts 
     (e.g.  to download commands to programmable function keys), you 
     answer Y for yes to this question.  If not, just hit RETURN.

          If you answer Y, you may choose between entering the command 
     directly or defining a file name containing the command string.  
     The latter is a good idea if the initialization string is long.

Send a reset string to the terminal?

          Here, you may define a string to be sent to the terminal 
     when FU.COM terminates.  The description of the initialization 
     command above applies here.

CURSOR LEAD-IN command:

          Cursor Lead-in is a special sequence of characters which 
     tells your terminal that the following characters are an address 
     on the screen on which the cursor should be placed.  

          When you define this command, you are asked the following 
     supplementary questions:

     CURSOR POSITIONING COMMAND to send between line and column:

         Some terminals need a command between the two numbers 
         defining the row and column cursor address.

     CURSOR POSITIONING COMMAND to send after line and column:
     
          Some terminals need a command after the two numbers defining 
          the row and column cursor address.

Column first?

          Most terminals require the address of the format: first ROW, 
     then COLUMN.  If this is the case on your terminal, answer N.  If 
     your terminal wants COLUMN first, then ROW, then answer Y.
 

OFFSET to add to LINE

      Enter the number to add to the LINE (ROW) address.

OFFSET to add to COLUMN

      Enter the number to add to the COLUMN address.

Binary address?

          Most terminals need the cursor address sent in binary form.  
     If that is true for your terminal, enter Y.  If your terminal 
     expects the cursor address as ASCII digits, enter N.  If so, you 
     are asked the supplementary question:

        2 or 3 ASCII digits?
   
          Enter the number of digits in the cursor address for your 
          terminal.

CLEAR SCREEN command:

          Enter the command that will clear the entire contents of 
     your screen, both foreground and background, if applicable.

Does CLEAR SCREEN also HOME cursor?

          This is normally the case; if it is not so on your terminal, 
     enter N, and define the cursor HOME command.

DELETE LINE command:

          Enter the command that deletes the entire line at the cursor 
     position.


INSERT LINE command:

          Enter the command that inserts a line at the cursor position.

ERASE TO END OF LINE command:

          Enter the command that erases the line at the cursor 
     position from the cursor position through the right end of the 
     line.

START OF 'HIGH-LIGHTING' command:

          If your terminal supports high-lighting (inverse video, 
     underline, etc.), then define the command that initiates the 
     high-lighting.  If this command is defined, the following 
     question is asked: 

END OF HIGH-LIGHTING command:

          Define the command that cancels high-lighting and sets the 
     screen to show characters in 'normal' video.

Number of rows (lines) on your screen:

          Enter the number of horizontal lines on your screen.

Number of columns on your screen:

          Enter the number of vertical column positions on your screen.

Delay after CURSOR ADDRESS (0-255 ms):
Delay after CLEAR, DELETE, and INSERT (0-255 ms):
Delay after ERASE TO END OF LINE and HIGHLIGHT On/Off (0-255 ms):

          Enter the delay in milliseconds required after the functions 
     specified.  RETURN means 0 (no delay).

Is this definition correct?

          If you have made any errors in the definitions, enter N.  
     You will then return to the terminal selection menu.  The 
     installation data you have just entered will be included in the 
     installation data file and appear on the terminal selection menu, 
     but installation will not be performed.  

     When you enter Y in response to this question, you are asked: 

     Operating frequency of your microprocessor in MHz (for delays):

          As the delays specified earlier are depending on the 
          operating frequency of your CPU, you must define this value.  

     The installation is finished, installation data is written to 
FU.COM, and you return to the outer menu.  New installation data is 
also saved in the installation data file and the new terminal will 
appear on the terminal selection list when you run FUINSTAL.DOC in 
future.
st