LSD.COM


This program lists the files in user areas ("groups") 0 to 7 on a disc in Drive A: and is
therefore suitable for use as a LocoScript Directory utility. It has been written in
assembly language to run under CP/M Plus on Amstrad PCW8256 or 8512 computers, using the
full width of the 90 column screen. It gives the option of either just displaying the
files on the screen, or simultaneously displaying and printing the list. The program
automatically sets up the PCW dot-matrix printer to print 90 character lines in draft
quality 12 pitch (Elite) on continuous (fanfold) paper. There is a message on the opening
screen telling the user what size of paper the printer is set to. Quality can be changed
to "High Quality" by means of the cursor and [+] key while in Printer Control, after
either loading paper or pressing [PTR]. This 90-column continuous paper setting is not
fixed as a default, so a Reset instruction will switch the printer back to its normal 80-
by-A4 single setting, or whatever other setting has been made the default, eg: by means
of SETPTR.COM.

LSD.COM will normally be made available in different forms, which will set the printer
either to:
		11 inch continuous paper -	LSD11.COM
or		12 inch      ditto		LSD12.COM
or		A4           ditto		LSDA4.COM
or		A4 single sheets		LSDSS.COM

Users may either fix upon one of these forms, renaming it LSD.COM and deleting the
others, or they may retain all forms and select whichever they require at any particular
time by using the full filename when calling up the program.


LSD.COM is designed to be copied from the program disc in Drive A: into Drive M:, and
will work from drive M: if SETDEF has been set properly (eg: by a suitable PROFILE.SUB)
to include the line:

		  setdef m:,* [order = (sub,com) temporary = m:] 

in which case the program disc must also carry SETDEF.COM as well as the PROFILE.SUB and
SUBMIT.COM files. The automatic copying of LSD.COM from the program disc into M:, by
means of instructions in PROFILE.SUB, will also require PIP.COM to be held on the program
disc.   By loading LSD.COM into M:, the program disc can be removed from Drive A: and
replaced by discs holding LocoScript1 or LocoScript2 files. A suitable PROFILE.SUB would
be:

		setdef m:,* [order = (sub,com) temporary = m:]
		pip m:=a:*.com[o]
		m:
		era setdef.com
		era submit.com
		a:


If a group has been given a group name in LocoScript, that name is actually held as an
empty file with a .GRP filetype ending. In the LSD program this name is printed
immediately after the group number, and is followed by the total number of files in that
group. Because the group name is itself a file, it will also be listed among the other
files in that group and also counts towards the total number of files on the disc. Drive
A:  discs normally hold no more than 64 files.

At the end of each disc's list will be given the total number of files in groups 0 to 7,
and the total number of k-bytes used in these files. LocoScript "limbo" files, which are
stored in user areas 8-15, are not included.

				How to use LSD:

Load LSD.COM, when running CP/M Plus and the A> prompt shows, by typing: lsd <return>. 
After an initial message, you will be invited to insert the disc to be read into Drive A:
and select D or P to Display or to Print & display the list of files. Once LSD has been
loaded you can continue selecting D(isplay) or P(rint and display), disc after disc,
until when you wish to quit you press Q to return to CP/M.

The version available from 25th October 1988 is version LSD 1.5. This version is free of
the known bugs present in earlier versions. It does not sort the files into alphabetical
order, a feature which it is hoped to add to later versions. I am not aware of any
unexpected faults or bugs in version 1.5 but no responsibility is accepted for any faults
which may be present, nor for any direct or consequential loss arising from its use.


Copyright (c) 1988 Martin H. Evans. . . . . . . . . . . . . . . . . . . . . . . . . . . 
111 High Street, Linton, Cambridgeshire CB1 6JT, England. . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .