80TRK.DOC
          TRiPsoft 02/04/88

A Library of files and programmes to implement an 80 track DS DD drive
as drive B: on Amstrad CPC computers running CPM+

Note that no responsibility is accepted for any loss or damage occuring
from the use of these programmes or the advice contained herein !

These programmes and patches have been tested on a 6128 and work with no
known faults.


SAFETY:   IF YOU HAVE TO CONSTRUCT A POWER SUPPLY OR CONNECT ONE TO YOUR 
                    AMSTRAD OR DISK DRIVE THEN BE CAREFUL !

       Mains voltages which are present on the input side of power supplies
         and in the monitor unit of the Computer are NOT FUNNY if you get
                              connected to them !

                         REMEMBER if in doubt DON'T !


CONTENTS:

        BPAT.SUB        Submit file to auto patch C10CPM3.EMS
        BPAT.HEX        data to be patched into above
        BPAT.Z80        source code for data
        BCPAT.SUB       Ditto for CPM3SEMI.EMS (as used by Dktronics
                        for their DRIVE C: Silicon disk)
        BCPAT.HEX       ---- do ----
        BCPAT.Z80       ---- do ----

        MLOAD.COM       Public domain loader programme used by .SUB files
        UNLOAD.COM      Public Domain un-loader programme ---- do ----

        FM.COM          Formatter programme for use after patching EMS file
        FM.Z80          Source code for above

        BDISK.COM       Programme to patch XDPB for drive B: for 80 trk use
        BDISK.Z80       Source code for above.


HOW TO GET STARTED WITH AN 80 TRACK DS DD DRIVE ON A 6128 ETC.

1.      Connect drive to Amstrad Disk expansion port using 34 way ribbon cable
        and 34 way edge connectors. Note a Half-twist is required in the cable
        as Amstrads pin no's do not coincide with Shugart's interface. So Pin
        1 (Amstrad) is connected to Pin 34 (Shugart).

2.      Remove any pull-up resistor pack from the 80 trk drive as this will
        load the Amstrads bus and is not needed as the internal drive is 
        'pulled up' already

3.      Check that your drive has a 'drive ready' signal on the appropriate
        line to the Amstrad. If not one will have to be provided. This can
        be achieved by a manual switch or better still a micro switch or
        photodiode/phototransistor to detect the presence of a disk in the 
        drive or the drive door being closed.

4.      Make up a suitable power supply for the drive. It is said that the
        Amstrad power supply can handle another drive but it is NOT a good
        idea ! Better to make a power supply for the whole machine and forget
        about the power from the monitor unit. The whole machine will work
        better and quieter and will last longer. The power supply needs to
        provide +5 volts and +12 volts well smoothed and regulated. Try
        computer junk shops for switched mode power supplies as these are 
        particularly good and are often avaiable from people who have up-
        graded IBM PC's with higher power supplies for hard disks etc.

5.      Having got all this together then plug it all in and turn on.
        Try running DISCKIT3 to format the drive as a 40 track unit and
        copy a few files back and forth to ensure the mechanics are working
        ok. At this stgae you will only be accessing 40 tracks SS and will
        show only 169k free or 178k free depending on whether you chose
        system or data format in DISCKIT3.

6.      If all has gone well then copy all the files from this Library
        onto a SYSTEM format disk along with your EMS file and SUBMIT.COM

7.      Boot up CPM+ from this disk and type:

        SUBMIT BPAT<return> (SUBMIT BCPAT if you use Dktronics silicon disk)

        The submit file should now operate and patch the EMS file for use
        with the new B: drive When this operation is finished copy the new
        EMS file onto a fresh system disk and re-boot CPM+

8.      If all boots up OK then put a disc in drive B: and type

        FM<return)

        You will now enter the formatting programme and should format
        any disks to be used in the B: Drive at this time.

9.      When formatting is finished re-boot cpm+ again.
        now type

        BDISK<return>

        You will be offered a menu of three formats under which the disk
        can be used. Select one by pressing A,B or C
        When the format has been patched into the XDPB the screen border will
        change colour to indicate the High capacity format 80 track system
        has been implemented.

10.     Check the free disk space on B: using SHOW or NSWP etc and verify
        that it conforms to your selected choice under BDISK

11.     Try copying some files from A: to B: and back and check that they
        do not become corrupted. If all is well then edit your PROFILE.SUB
        start up file to include the line:

        BDISK B (or A or C) so as to auto select the correct format for
        using the B Drive.

12.     Enjoy using the disk space ! Up to 796 k free depending on choice
        of format.

                    Good luck with the programmes.
.endes to implement an 80 track DS DD drive
as drive B: on Amstrad CP