M A K E A S M
			=============


	MAKEASM V 1.0  1/88 (C) D.Langenohl



 This program  converts  listfiles  (.PRN)  created  by  then  PD 
assembler  ZMAC to sourcefiles for the JRT assembler JRTASM.  For 
JRTASM is, unlike ZMAC, an 8080-assembler it does not  understand 
Z80 mnemonics.  Nevertheless it can treat Z80 code, provided that 
it is presented in db (defb),  dw (defw) or ds (defs) statements.  
This is done by MAKEASM. 


 The way how to create an INT-file:

1.)  Take your editor and write the sourcelisting for ZMAC.
     
     Restrictions:  - no globals !
                    - no ORG (AORG,RORG) statements !
                    - max 4 db's in a line ! For example :
                      db 'This'
                      db ' is '
                      db 'corr'
                      db 'ect '
                      db ' !$'
                      This is because only the first 4 Bytes will
                      appeare in the PRN-file, and not a fault of 
                      MAKEASM !
                    - max  2 dw (or defw) statements in  a  line, 
                      for the same reason.
                    - no  ds  (or defs) at the end of the  source 
                      unless   followed  by  another   (not   ds) 
                      statement. For example:
                      NOT:     ds 100
                               end

                      BUT:     ds 99
                               nop
                               end          
        
     No  need  to insert the entry code for JRTASM,  this can  be 
     done by MAKEASM much faster.

2.) Make a PRN-file by  ZMAC ,filename=filename(.EXT).
    ZMAC  will  expect  the  extension  ASM  as  default.  It  is 
    advisable  to use another extension to prevent any confusion, 
    because for JRTASM the extension ASM is a must.

3.) Now  type  MAKEASM.  You  will first to  be  asked  for  the 
    filename.  If no extension is applied MAKEASM will search for 
    a PRNfile.  Next you can choose some options . Press ENTER if 
    none of them desired. The options are :
          I - this will insert the entry code.
          P - the listing will be send to the printer.
          S - the listing will be shown on screen.  To stop  the 
              printing press any key, to continue press SPACE.
          N - None of the above.
   You  may type in this options in any order, with spaces or any 
   charakters between them or not.             
   The  original sourcecode of ZMAC will be included as  comments 
   to make any debugging easier.
   Now you have got an ASMfile which can be treated by JRTASM.
   You  will now be asked for another filename.  Press  ENTER  to 
   leave MAKEASM.

4.) EXEC JRTASM ..... 
    The result is the desired INT-file.


 MAKEASM  is written in TURBO-PASCAL and therefore will run  only 
on Z80 systems.


     Please report any bugs to :   DIETMAR LANGENOHL
                                   Hussitenstr.4-5/A8
                                   1000 BERLIN 65

IETMAR LANGENOHL
                                   Hussitenstr.4-5/A8